[Speaker Notes: %\printinunitsof{cm}\prntlen{\textwidth}]

---
[Speaker Notes: Note that before quantum physics we had ``classical'' physics. Similar, we will differentiate between quantum computers and classical computers (those that we know and use everyday). Also, roughly, quantum physics and quantum mechanics means the same thing in this discussion, and we refer to quantum-mechanical systems. \\~\ To arrive at an explanation of a quantum computer, as well as quantum cryptography, we will step through some of the basic principles/ideas. First we will look at how information is represented in]

---
[Speaker Notes: A bit is defined, in an informal manner, just for reference.]

---
[Speaker Notes: The key distinguishing feature of qubits compared to bits is that qubits have many possible states, not just 0 and 1. \\~\ The notation used is not so important here; it is just a short way that we can identify the two basis states which are similar to bit 0 and bit 1. We will see next how the qubit is expressed when in the ``in between'' states.]

---
[Speaker Notes: Superposition is a concept seen in other systems, but quantum superposition is the main concept that delivers powerful innovations with quantum computers.]

---
[Speaker Notes: You may think of the concept as superposition as follows. A classical bit has the value 0 or 1. A qubit has the value of 0 or 1, or a value that is both 0 and 1 at the same time. \\~\ An important point is that the weights, $\alpha$ and $\beta$, can be controlled. This is the key part of how qubits are used in calculations, as next we see that measuring a qubit returns 0 or 1 with some probability.]

---
[Speaker Notes: There are two important issues about measuring a qubit. First, the result will either be 0 or 1. However when the qubit is in a superposition state of $\alpha|0\rangle + \beta|1\rangle$, then we don't know in advance which value will be output from the measurement. But we do know that with probability $\alpha^2$ it will be bit 0 and with probability $\beta^2$ it will be bit 1. By controlling the weights, $\alpha$ and $\beta$, we can increase the probability that a useful output will be measured. \\~\ The other issue is that upon measurement, the qubit reverts to one of the basis states. It will no longer be a superposition of states.]

---
[Speaker Notes: Quantum entanglement is another concept, which you may hear about when referring to quantum communications and quantum teleportation. We will not cover it in any depth here, but present a simple example in the following. \\~\ Entanglement can be achieved for example by firing a laser at a crystal that causes two photons to split but be entangled.]

---
[Speaker Notes: Experiments have had qubits entangled over distances of 10's of kilometres.]

---
[Speaker Notes: This definition of quantum computation is quite vague. How are the states of the qubits modified? Using logic gates to form circuits. One point to note is that at the end the result is measured. As noted before, measuring a quantum system will return some binary value with some probability \emph{and} collapes any superpositions. This means that any speed up to be potentially be obtained by quantum computing needs to be done before the measurement.]

---
[Speaker Notes: Note that AND and NOT gates are the universal set: everything else can be built from them.]

---
[Speaker Notes: A single-bit gate takes a single qubit as input and produces a single qubit as output.]

---
[Speaker Notes: We are only covering a digital quantum computer. The topics of quantum simulation and quantum annealing are not covered here.]

---
[Speaker Notes: For example, if the two qubits are constructed so that $\beta = 0$ and $\delta = 0$, and $\alpha = \gamma = 1/\sqrt{2}$, then there is 50\% probability of measuring 00 and 50\% probability of measuring 10. There is no chance of measuring 01 or 11.]

---
[Speaker Notes: The parallelism that can be achieved is the promising feature of quantum computing. The following example aims to illustrate the idea.]

---
[Speaker Notes: The above example used decimal values, but also consider their binary values, i.e.\ the function is applied to 8 values: 000, 001, 010, 011, 100, 101, 110 and 111.]

---
[Speaker Notes: While this a contrived example with many real flaws, it aims to demonstrate that quantum parallelism is achieved by the fact that the quantum calculation is one all states of the quantum register, rather than just a single value as in classical computing. \\~\ You should already recognise a problem with the above example. While the output quantum register contains qubits in a superposition that contains information about all 8 answers, when we measure the output register we get just one of those answers with some probability, i.e.\ the measurement problem. If the probabilities were all equal, i.e.\ 12.5\%, then when we measure the output we would get a value of 000 with probability 12.5\%. If we did it again, we may get 011 with probability 12.5\%. So the answer is essentialy useless to us; we'd need to calculate 8 times, resulting in the same effort as a classical computer. Quantum algorithms are designed so that the weights/probabilities of the output do give the ``correct'' answer with high probability.]

---
[Speaker Notes: The main point to note is that ``quantum'' algorithms actually are a hybrid of classical algorithms and quantum calculations.]

---
[Speaker Notes: Grover's search algorithm can be used for a brute-force attack. For example with a symmetric key cipher, assume we have a function that decrypts the ciphertext and returns true of the obtained plaintext is correct.]

---
[Speaker Notes: \tablename~\ref{table:groversearch} shows worst case number of attempts a brute-force attack on a key , using either a classical algorithm or Grover's quantum search algorithm. Note that $\sqrt{2^N} = 2^{N/2}$. While the quantum algorithm produces a significant speedup, with regards to protecting symmetric key ciphers against brute force attacks using quantum computers, an easy solution is to double the key length. That is, if a 128-bit key was recommended as secure against brute force attacks using today's classical computers, then to be secure against brute force attacks with future quantum computers, use a 256-bit key. While using a double length key incurs a performance drop for AES, it is not so substantial that makes AES too slow to use, and does not require a new algorithm design.]

---
[Speaker Notes: \\~\]

---
[Speaker Notes: The paper \href{http://doi.acm.org/10.1145/2494568}{A Blueprint For Building a Quantum Computer} by Rodney Van Meter and Clare Horsman, published in Communications of the ACM, October 2013, has compared the speeds for specific implementations of algorithms on classical and quantum computers. Note that the following results are mainly theoretical, estimating the performance based on several actual measurements with smaller numbers.]

---
[Speaker Notes: \figurename~\ref{fig:quantum:nfsshor} shows estimated time to factor a L-bit number. The number field sieve on the solid black line is using a classical computer. The cross on that line is for the point of L=768 bits and 3300 CPU years. The NIST recommended key length is L=2048 bits. The lines labelled with Shor are using a quantum computer. The four lines for Shor are different algorithms and architectures, as well as different quantum clock speeds (1Hz vz 1MHz). \\~\ One way to read the figure is to look at the number of bits that can be factored in 1 year. A 1GHz classical computer using number field sieve could factor a 500 bit number. A quantum computer using Shor's algorithm and with a 1 Hz clock could factor a 80 bit number. But with a 1 MHz clock it could factor a 8000 bit number.]

---
[Speaker Notes: \figurename~\ref{fig:quantum:threat}, from the \href{https://globalriskinstitute.org/publications/quantum-threat-timeline/}{Quantum Threat Timeline Report}, shows the opinions of 22 quantum computing experts. Most think quantum computing will not be a threat to public-key cryptosystems in the next 5 years, and more than half, also in the next 10 years. Almost all think there is a 50\% or greater chance that quantum computing will threaten RSA in the next 20 years.]

---
[Speaker Notes: Increasing the time that qubits can hold their coherent state is one practical aim of quantum computing. See the T2 column in the \href{https://quantumcomputingreport.com/scorecards/qubit-quality/}{Quantum Computing Report} for example values.]

---
[Speaker Notes: Error correcting schemes introduce an overhead, and one concern is that the overhead needed to deal with errors may mean quantum computing does not produce significant advantages over classical computing.]

---
[Speaker Notes: \figurename~\ref{fig:quantum:googleerror}, taken from \href{https://ai.googleblog.com/2018/03/a-preview-of-bristlecone-googles-new.html}{A Preview of Bristlecone, Google’s New Quantum Processor} by Google Quantum AI Lab, illustrates the conceptual relationship between error rates and qubits. The error correction threshold indicates error rates below this are needed for error correction to work.]

---
[Speaker Notes: \\~\]

---
[Speaker Notes: \\~\]

---
[Speaker Notes: Note that while quantum computers can be used to break cryptographic mechanisms (e.g.\ using Schor's algorothm), quantum cryptography is separate topic of quantum systems that is about creating cryptographic mechanisms. Quantum cryptographic mechanisms will use quantum computers.]

---
[Speaker Notes: For a formal explanation of QKD, with an example see: \url{https://www.cse.wustl.edu/~jain/cse571-07/ftp/quantum/} or the original paper on one scheme BB84 at \url{https://doi.org/10.1016/j.tcs.2014.05.025}.]

---
[Speaker Notes: \figurename~\ref{fig:quantum:bb84} is taken from the \href{https://doi.org/10.1016/j.tcs.2014.05.025}{original 1984 article by Bennet and Brassard}, which was re-published by Elsevier in the journal Theoretical Computer Science in 2014. BB84 is a scheme still used for quantum key distribution. The paper, in section III, has a nice explanation of the protocol.]

---
[Speaker Notes: The security of quantum key distribution depends on that measurement problem, i.e.\ that measuring a quantum superposition state, changes the state. The attacker cannot measure the communications between A and B without changing the communications. It is easy for A and B to recognise if the communications have been changed.]

---
[Speaker Notes: \\~\]