A has 5 bits to transmit to B
4.5km link
500kb/s data rate
What is the total delay of delivering the information?

---
Two components of delay:
1. Transmission delay
2. Propagation delay
(Assume processing and queuing delays are very small, i.e. 0)

---
What is the transmission delay?

---
How long to transmit 1 bit?

---
How long to transmit 1 bit?
Data rate is 500kb/s
Transmission time of 1 bit is 2us

---
Transmission delay is 10us

---
What is the propagation delay?

---
How long for signal to propagate from A to B?

---
How long for signal to propagate from A to B?
4.5km at 3x108m/s is 15us

---
B receives all 5 bits at time 25us
Total delay is 25us
(10 us transmission delay +
15 us propagation delay)