Isotropic antenna. Transmit with power Pt. Power received at all points 1m away is Pr

---
Directional antenna. Transmit with power Pt. Power received at all points on blue line
is Pr (the same power level as 1m away from isotropic)

---
At the red point (1m away from directional antenna), power received is Px.
Px is greater than Pr

---
The gain of the blue directional antenna is the ratio between power received 1m away
From directional antenna (Px) and power received 1m away from isotropic antenna (Pr)