Data rate: 1 Mb/s
Payload: 1000 B
Header/ACK: 50 B
Speed of light: 3x108 m/s

---
Propagation delay: 36,000 km @ 3x108 m/s = 120 ms
DATA transmission delay: 1050 B @ 1 Mb/s = 8.4 ms
ACK transmission delay: 50 B @ 1 Mb/s = 0.4 ms
Stop and Wait (Window = 1)
Time to receive ACK: 8.4 + 120 + 0.4 + 120 = 248.8 ms
Real data delivered: 1000 B
Throughput: 1000 B / 248.8 ms = 32,154 b/s
Efficiency: 32,154 b/s out of 1 Mb/s = 3.2 %

---
Propagation delay: 36,000 km @ 3x108 m/s = 120 ms
DATA transmission delay: 1050 B @ 1 Mb/s = 8.4 ms
ACK transmission delay: 50 B @ 1 Mb/s = 0.4 ms
Sliding Window (Window = 7)
Time to receive ACK: 8.4 + 120 + 0.4 + 120 = 248.8 ms
Time to send window of frames: 7 x 8.4 = 58.8 ms
Real data delivered: 7000 B
Throughput: 7000 B / 248.8 ms = 225,080 b/s
Efficiency: 225,080 b/s out of 1 Mb/s = 22.5 %

---
What size window to achieve highest efficiency?
Time to receive ACK: 248.8 ms
DATA Transmission delay: 8.4 ms
Aim: continuously send DATA frames (no waiting)
DATA frames in time to receive ACK: 248.8 / 8.4 = 29.6
Window size of 30 frames is sufficient
With 5 bit sequence number, maximum window size is 31 frames
W = 31:
Efficiency: 1000 B / 1050 B = 95.2 %
Throughput: 952,381 b/s

---
Window size