Free Technology Workshop
Hacking
Hands on with wireless LAN routers,
packet capture and wireless security
Organised by Steven Gordon
Bangkadi 3rd floor IT Lab
10:30-13:30 Friday 18 July 2014
http://ict.siit.tu.ac.th/moodle/
  _______ ________ __
 | |.-----.-----.-----.| | | |.----.| |_
 | - || _ | -__| || | | || _|| _|
 |_______|| __|_____|__|__||________||__| |____|
        |__| W I R E L E S S F R E E D O M

---
Aims
- Understand what is a “wireless router”
- See the internals (hardware)
- Know about (open source) firmware
- Understand what is a “wireless LAN”
- Setup a wireless LAN
- Aware of security features in wireless LANs
- Capture wireless packets (“sniffing”)
- Bypass security features in wireless LANs

---
Sources
- openwrt.org
- wikipedia.org
- and others

---
Naming, Acronyms, etc.
- AP - access point
- BSSID - basic SSID	identifies AP
- CTS - clear to send
- ESSID - extended SSID	identifies network (also SSID)
- LAN - local area network
- MAC - medium access control (layer)	defines how to share channel with others
- NAT - network address translation	allows private addressing in internal network
- PHY - physical (layer)	defines data rate, channels, power, signals, ...
- RTS - request to send
- SSID - service set identifier
- WAN - wide area network
- WEP - wired equivalent privacy	insecure encryption
- WLAN - wireless LAN	also WiFi, IEEE 802.11
- WMM - wireless multimedia mode	priority for voice, video packets
- WPA - WiFi protected access	secure encryption
- WRT - wireless router

---
Quick Reference
- Router IP: 192.168.1.1
- Router username: root
- Router password: s11tnetw0rk
- Router name and SSID: ICTRxx (xx=10, 11, ...)
- iMac username: student
- iMac password: student
- Software: http://ict.siit.tu.ac.th/software/
- Workshop: http://ict.siit.tu.ac.th/moodle/

---
Wireless Routers

---
Removable antennas
LAN ports
Reset
Internet (WAN) port
Power

---
Wireless Router at Home
192.168.1.2
192.168.1.1
Modem
192.168.1.3
120.6.46.15
telephone line
to ISP
192.168.1.5
192.168.1.4
internal LAN with private IPs
Internet connection with public IP

---
Wireless All-in-one Router at Home
192.168.1.2
192.168.1.1
192.168.1.3
120.6.46.15
telephone line
to ISP
192.168.1.5
192.168.1.4
internal LAN with private IPs
Internet connection with public IP

---
Wireless LAN AP at SIIT
Link to ISP
SIIT internal network with private IPs
203.131.209.66

---
Wireless Router
Ethernet
switch
Router
with
firewall, NAT,
web server,
SSH server,
DHCP server,
...
Ethernet
WAN port
WLAN
access point
external
network
internal
network

---
Wireless Router
with ADSL Modem
Ethernet
switch
Router
with
firewall, NAT,
web server,
SSH server,
DHCP server,
...
ADSL
Modem
WLAN
access point
external
network
internal
network

---
Wireless AP
Ethernet
port
Bridge
WLAN
interface
internal
network

---
Router
All-in-one
AP

---
Removable antennas
LAN ports
Reset
Internet (WAN) port
Power

---
Linksys WRT54G(L)
Since 2003, popular wireless router with Linux firmware
supports 3rd party firmware
- CPU: Broadcom 200MHz
- Flash: 4MB
- RAM: 16MB
- Wireless chip: Broadcom (integrated)
- Wireless PHY: 11b, 11g
- Wireless Tx Power: 63 mW
- Antenna: 2 x 2.2dBi dipole
- Wired ports: 5 x 10/100Mb/s
32-bit MIPS
Non-volatile storage
Volatile storage
CPU + WiFi + Switch
Up to 54 Mb/s
Adjustable
Removable RP-SMA
4 x LAN + 1 x WAN

---
RAM
Broadcom CPU
Flash Memory

---
Wireless LANs

---
Wireless LANs
- IEEE 802.11 (standards), WiFi (marketing)
- Aim: Provide equivalent functionality to wired Ethernet
- Advantages of wireless:
  - No wires
  - Mobility
- Disadvantages of wireless:
  - More errors, varying delay: hard to achieve same performance as wires
  - Spectrum/frequencies available is limited: cannot just add more wires
  - Radio transmissions are broadcast: No “physical” security

---
Wireless LANs: Broadcast Radio
B
transmission range
A
C
D
- Transmit signal at center frequency f, with bandwidth BW
- Devices with receives tuned to frequency f will receive the signal (if it has strong
  enough power)
- “Strong enough power”: depends on transmit power, receiver characteristics,
  antennas, frequency, obstructions
- Assume maximum distance some signal can be transmitted is range

---
Wireless LANs: Broadcast Radio
- Everyone within range of transmitter receives the signal
- If two (or more) signals received at same time, then neither can be understood
  - Interference, a “collision” occurs
- IEEE 802.11 MAC protocol aims to ensure only one device transmits at a time
  - Good: No (or few) collisions
  - Bad: Each device must wait for other devices before it can send
    - Shared medium: divide the data rate by number of devices wanting to share

---
IEEE 802.11 Wireless LANs
- Access Point (AP): acts as a bridge between wireless segment (WiFi) and wired segment (Ethernet)
- Client: wireless communications to AP
C1
Wired network
AP
C2
C3

---
IEEE 802.11 Wireless LANs
- Physical (PHY) Layer:
  - Defines how to send wireless signals between devices
  - Data rate, frequency, bandwidth, power, modulation, ...
  - Different standards: 802.11a, 802.11b, 802.11g, ...
- Medium Access Control (MAC) Layer:
  - Defines how to efficiently send data between devices while sharing the medium
  - Common across different PHY standards

---
Wireless LAN PHY Characteristics
www.microwavejournal.com

---
Channels in 2.4 GHz Band
- 2.4 GHz ISM Band: 2.400 - 2.485 GHz
- Channel Bandwidth: ~20 MHz
- 11n, 11ac use larger bandwidth for higher data rate

---
5 GHz band allows for more non-overlapping channels and has less interference

---
Wireless LANs: Key Points
- Data Rate
  - Speed at which data sent between 2 devices
  - Varies according to PHY and distance
- Throughput:
  - MAC Overheads, e.g. headers, ACKs: 20-40%
    - 54 Mb/s - 25% overhead = 4 Mb/s
  - Waiting for others: divide by number of users
    - 10 users associated with AP: 4 Mb/s per user

---
Wireless LANs: Key Points
- Frequency Bands:
  - 2.4 GHz: supported by all devices; crowded
  - 5 GHz: not all APs, clients support; shorter range; less interference
- Channels:
  - Important when many nearby APs
  - 2 APs, 20 clients split amongst the APs
  - APs use same channel: 2 Mb/s per user
  - APs use non-overlapping channels: 4 Mb/s per user
  - 2.4 GHz band: channels 1, 6 and 11 (and 14)
  - 5 GHz band: 8 non-overlapping channels

---
Wireless LANs: Key Points
- Security:
  - None: no authentication or encryption
  - WEP: shared secret key, flawed
  - WPA: shared secret key (client and AP)
  - WPA Enterprise: authentication performed between client and separate server, encryption between client and AP

---
Wireless Router Firmware

---
WRT54GL Flash Memory
4096KB = 4MB
256K
1739K
64K
501K
1536K
Kernel
Root file system
Root data
Bootloader
NVRAM
- Bootloader: loads firmware image into RAM, reads parameters from NVRAM
- Firmware image:
  - Linux Kernel
  - Root file system, e.g. permanent applications and libraries
  - Root data, e.g. config files, installed applications
- NVRAM: configurable parameters only used by bootloader
How to see this info? cat /proc/mtd and/or dmesg

---
Wireless Router Firmware - Normal Operation
- When router boots, bootloader loads firmware (kernel + root + data) into RAM and executes kernel
- Permanent changes can be written to “root data” on Flash
  - Edit configuration files
  - Install new applications
- Non-permanent changes can be written to temporary file system in RAM
  - Log files

---
Wireless Router Firmware - Flashing New Firmware
- Bootloader can be used to write a new firmware image
  - Replace kernel + root file system
- Two common options:
  - Existing firmware image has option to replace itself
  - Bootloader includes simple application (TFTP) to allow transfer of firmware image to device upon boot
- Next time the device boots, bootloader loads the new kernel + root file system

---
Wireless Router Firmware
- All wireless routers come with manufacturer provided firmware
  - Based on Linux and other embedded OS
- 3rd party firmware projects, usually Linux-based
  - OpenWRT: configurable with latest developments, free, open source software
  - DD-WRT: based on OpenWRT, ready-to-use, includes proprietary components
  - Tomato: ready-to-use, includes proprietary components
  - and others

---
OpenWRT
- Open source Linux distribution for embedded network devices
- Base packages provided as downloadable firmware image for many different devices
- Package manager (opkg) allows additional packages to be installed
- Different versions:
  - 14.07 Barrier Breaker
  - 12.09 Attitude Adjustment
  - 10.03 Backfire
  - 8.09 Kamikaze

---
Challenges with OpenWRT (and other 3rd party firmware)
- Only work for selected wireless routers, primarily those that use Linux-based manufacturer firmware
- Delay between release of new router and firmware image release
- Without open source drivers (or binary drivers provided by chip manufacturers) router features may not work
  - E.g. 802.11ac drivers are not yet common
- Performance with open source drivers may be worse (or better!) then manufacturer drivers

---
Mac OSX Command Line

---
Mac OSX File Sharing
- File Sharing
  - System Preferences → Sharing
  - File Sharing: On
- Connect to another iMac:
  - Finder → Shared → iMac_xx
- Public Shared Directory:
  - Yours: /Users/student/Public
  - Theirs: /Volumes/student's Public Folder
- Create 20 MB random file in Terminal:
  $ dd if=/dev/urandom of=rand.bin bs=20m count=1

---
Mac OSX Commands
- Time a command on Terminal:
  $ cd /Volumes/students' Public Folder
  $ time cp rand.bin ~/
  real 0m8.804s
  ...
- View interfaces (en0 Ethernet, en1 WiFi):
  $ ifconfig en1
- Change MAC address:
  $ sudo ifconfig en1 ether aa:bb:cc:11:22:33

---
Mac OSX Software Installs
- http://ict.siit.tu.ac.th/software/osx/
- XQuartz (needed by Wireshark)
- Wireshark

---
Mac OSX Packet Capture
- Link to airport:	(only needed once)
  sudo ln -s /System/Library/PrivateFrameworks/Apple80211.framework/Versions/Current/Resources/airport /usr/local/bin/airport
- Search for active channels:
  $ sudo airport en1 -s
- Start capture on channel 6:
  $ sudo airport en1 sniff 6	(Ctrl-C to quit)
- View the .cap file with tcpdump or Wireshark

---
Example Wireless Networks

---
Setup the Wireless Router
- Explore OpenWRT web interface
  - View Stats: Status → Realtime Graphs → ...
  - Config Wifi: Network → Wifi → Edit → ...
  - Install software: System → Software →...
  - Edit firewall: Network → Firewall → ...

---
Measure Performance
imac1
imac2
- Compare delay across Ethernet vs WiFi
  - imac1: ping 192.168.1.1
  - imac2: ping 192.168.1.1
- Measure throughput across WiFi
  - Setup File Sharing on iMacs
  - imac1: Create 20MB random file in Public directory
    $ dd if=/dev/urandom of=rand.bin bs=20m count=1
  - imac2: Copy file from imac1 shared directory to home
    $ time cp /Volumes/students' Public Folder/rand.bin ~/

---
Intercept Other Peoples Data
wsiit AP
imac2
imac1
- iMac1: Start packet capture
- iMac2: Access website (via SIIT internet)
- iMac1: Stop packet capture and view .cap file in Wireshark
  - Filter by 'http' and/or 'ip==10.10.x.y'

---
Use Wireless Router as Client
wsiit AP
- In OpenWRT web interface:
  - Network → Wifi → Scan
    - Join Network
    - Default parameters (wwan, …)
    - Save and Apply
- Now use iMac to access SIIT internet via router

---
Setup a Rogue AP and Redirect HTTPS Login Web Pages to Unencrypted HTTP Logins
?